## Slide 1
Future Circular Collider (FCC)
Europe’s Next-Generation Flagship Particle Physics Project at CERN
Andreas Hoecker (CERN), Les Rencontres de Noirmoutier, 3 June 2026

## Slide 2
Future Circular Collider (FCC)
Europe’s Next-Generation Flagship Particle Physics Project at CERN
Andreas Hoecker (CERN), Les Rencontres de Noirmoutier, 3 June 2026
High-energy physics has an environmental footprint driven by high power demands, large-scale infrastructures, and specialised detector technologies
Unlike previous large-scale accelerator projects, sustainability considerations have been integrated into the FCC design from the outset
Sustainability involves environmental impact, economic viability, and societal benefit
In this talk, I will introduce the project and its scientific goals, while highlighting the associated environmental challenges along the way

## Slide 3
The European Strategy for Particle Physics
Open Symposium, European Strategy of Particle Physics, 23–27 Jun 2025, Venice Lido [Link]

## Slide 4
The European Strategy for Particle Physics
Cornerstone of Europe’s decision-making process for the long-term future of the field
Mandated by CERN Council, the Strategy is formed through a broad consultation of the particle physics communities in Europe and worldwide (266 individual and national submissions, 2-year process)
In the Strategy process, recommendations are developed which are submitted to the CERN Council for an update of the Strategy
It is not a project approval process; projects are approved by the CERN Council through a separate decision process, taking the Strategy recommendations into account
Original Strategy (2006): LHC, mooting of luminosity upgrade of LHC, R&D in accelerator technologies, coordination with a potential ILC project
1st Update (2013): High Luminosity LHC, need for a post-LHC programme
2nd Update (2020): FCC feasibility study
3rd Update (2026): Recommendation for the next large-scale accelerator project at CERN

## Slide 5
The European Strategy for Particle Physics
Main recommendations of the 2026 strategy update
The full exploitation of the physics potential of the LHC and the HL-LHC and the completion of the high-luminosity upgrade remain the highest priorities of European particle physics. Every effort must be made to complete the HL-LHC upgrade within the current schedule
The electron–positron Future Circular Collider (FCC-ee) is recommended as the preferred option for the next flagship collider at CERN
A descoped FCC-ee* is the preferred alternative option for the next flagship collider at CERN *No ttbar run: –1.26 BCHF, drop 2 / 4 experiments: –0.80 BCHF, decrease RF power from 50 → 30 MW (–0.35 BCHF)
The particle physics community should continue and intensify its efforts to develop and adopt sustainable solutions
…
Links: CERN Council resolution, Recommendations, Briefing book, All documents, More information, CERN Colloquium by Karl Jakobs

## Slide 6
Large Hadron Collider (LHC) at CERN: the world’s largest accelerator reaching unprecedented energy and intensity
6
27 km underground accelerator and collider
Superconducting magnets (1.9 K = –271.3 °C) steer the particles around the ring
Proton and ions are accelerated to multi-TeV scale energies before they collide

## Slide 7
Presentation
ATLAS
LHCb
ALICE
ATLAS
ALICE
CMS
LHCb
LHC
SPS
PS
LHC and Experiments
Aerial view
CMS
All experiments are global collaborations

## Slide 8
Presentation
ATLAS
LHCb
ALICE
LHC
SPS
PS
Aerial view
CMS
FASER
SND
MoEDAL
MilliQan
LHCf
FASER
SND@LHC
PRL 134 (2025) 21
LHC and Experiments

## Slide 9
Presentation
ATLAS
LHCb
ALICE
LHC
SPS
PS
Aerial view
CMS
FASER
SND
MoEDAL
MilliQan
LHCf
PRL 134 (2025) 21
LHC and Experiments
LHC, experiments, software & computing, object reconstruction and physics analysis — all perform beyond design. Many new analyses ideas emerged that were not thought of during the design phase. ML now ubiquitous

## Slide 10
Presentation of Higgs boson discovery by ATLAS and CMS at CERN on 4 July 2012
A monumental discovery

## Slide 11
Presentation of Higgs boson discovery by ATLAS and CMS at CERN on 4 July 2012
A monumental discovery

## Slide 12
The fundamental universe is profoundly strange
The sub-atomic structure of matter and its interactions is described by the Standard Model (SM)
Spin 1/2

## Slide 13
The fundamental universe is profoundly strange
The sub-atomic structure of matter and its interactions is described by the Standard Model (SM)
Spin 1/2
Spin 1
Spin 0
Particles discovered through decades of international, high-technology accelerator-based research

## Slide 14
The fundamental universe is profoundly strange
The sub-atomic structure of matter and its interactions is described by the Standard Model (SM)
Spin 1/2
Fermion mass pattern (“flavour problerm”)
CERN Courier
top quark 340,000 times heavier than electron

## Slide 15
The fundamental universe is profoundly strange
The sub-atomic structure of matter and its interactions is described by the Standard Model (SM)
Spin 1/2
Spin 1
Spin 0

## Slide 16
The fundamental universe is profoundly strange
The sub-atomic structure of matter and its interactions is described by the Standard Model (SM)
Spin 1/2
Spin 1
Spin 0
New kind of interactions, unlike any known force
A manifestation of a vacuum field that gives elementary particles mass according to their coupling strength
The core conceptual challenges of the SM are tied to the Higgs sector (unstable mass)
The Higgs may also hold clues to dark matter, matter–antimatter asymmetry, and physics beyond the SM (eg, is the Higgs boson elementary? Does it have brothers and sisters? …)

## Slide 17
The LHC showed that the Brout-Englert-Higgs mechanism is real
Discovery of Higgs boson enables the direct study of electroweak symmetry breaking and the process of mass generation
ATLAS: ATLAS-CONF-2025-006, CMS: arXiv:2602.18611
Unpleasant scalar sector (23 parameters, large hierarchy) — key to many mysteries
+ ….
H
H
H
f
f
H
H
W/Z
W/Z
Coupling strength modifiers:

## Slide 18
We have learned so much more at the LHC …
A plethora of measurements, some involving extremely rare and sensitive processes, others reaching very high precision, confirm the predictive power of the SM and deepen our understanding
82 new hadronic bound states discovered so far, 28 of which exotic, the heaviest being toponium
Heavy-ion collisions enabled unprecedented insights into the quark-gluon plasma
Searches for new phenomena have set tight constraints on some of the most popular SM extensions, thus completely changing the field of beyond the SM physics
Phys. Rep. 1116 (2025) 261
PRD 105 (2022) 012010

## Slide 19
The HL-LHC will use new technologies to provide 6 times more collisions than the LHC
Intensities require large-scale detector upgrades
Access to rare phenomena, greater precision and new discovery potential (350M H, 240k HH, 13B top, 720M WW, …)
It will start operating in 2030 and run until 2041
Complementary in many ways to the FCC-ee
Upgrade to the High-Luminosity LHC is under way
Notes: Additional information (OPTIONAL, TIME PERMITTING)
Key innovations in HL-LHC:
1) Powerful superconducting quadrupole magnets (12 Tesla) will be installed on either side of the ATLAS and CMS experiments to focus the particle bunches. These magnets will be made using niobium-tin (Nb3Sn), used for the first time in an accelerator (instead of niobium-titanium)
2) Crab cavities for tilting the beams (16 in total) - give the head and tail of the particle bunches opposite-sign transverse momentum before they meet, enlarging the overlap area of the two bunches and thus increasing the probability of collisions.
3) One hundred new, more effective collimators will be installed: these devices absorb particles that stray from the beam trajectory and might otherwise damage the machine.
4) More compact and powerful bending magnets (11 Tesla), also made using the niobium-tin superconductor.
5) Innovative superconducting power lines will connect the power converters to the accelerator; will be able to carry currents of record intensities, up to 100 000 amps!

## Slide 20
Environmental impact of LHC / HL-LHC operation
CERN’s total annual power consumption is ~1.3 TWh dropping to ~0.4 TWh when LHC is not operating
Scope 1: direct emission of greenhouse gases*
Scope 2: indirect emission via purchased electricity
Scope 3: all other indirect emission (procurement, …)
Source: CERN Environmental Report 2023–2024
*F-gas impact mainly from RPC losses and detector cooling; HL-LHC reductions from leak repairs, gas dilution, and new CO2 cooling plants
Total of 350 kt CO2e in 2024

## Slide 21
Future Circular Collider
90.7 km circumference tunnel facility to host an e+e– and a hadron collider
Feasibility study: 3 volumes (physics & experiments, accelerator, civil engineering & sustainability) (March 2025), All documents

## Slide 22
Proposed large-scale projects at CERN, ~ 2045

## Slide 23
Assessment of proposed colliders by expert group
[Link to ESG WG2a report]
Muon Collider: Technologies in early phases of exploration, large R&D programme defined (300 MCHF, 1800 FTEy), demonstrator required
FCC-hh: Further R&D and industrialisation with cost reduction of high-field magnets (Nb3Sn 15–20 y, HTS ?)
LEP3: No detailed lattice design & full-scale simulation, proposed baseline HTS nested quadrupoles/sextupoles has lowest TRL
LHeC: Performance relies on very high current Energy-Recovery Linac (ERL), large luminosity uncertainty, PERLE @ IJCLab required
(1–9)

## Slide 24
Assessment of physics reach
[Link to ESG WG2b report]
SM
BSM
e+e– colliders only
pp (+ e+e–) collider
μμ (+ e+e–) collider
High-E e+e– collider

## Slide 25
A remark on CEPC
CEPC — China
CEPC — Circular (not Chinese !) Electron Positron Collider
Very similar to FCC-ee: baseline is 100 km tunnel, top-up, 30 MW / beam, 2 IPs, option for subsequent hadron collider
CEPC proposal was submitted to Chinese Academy of Science for inclusion in 15th 5-year plan in 2025, but not retained (STCF preliminarily yes)
CEPC plan: hope to retain funding, seek collaboration with FCC-ee, resubmit in 2030 if FCC-ee not approved by then
Total cost 4.6B USD
CEPC TDR: arXiv:2312.14363
Detector TDR: arXiv:2510.05260

## Slide 26
FCC-ee
Next-generation circular e+e– collider to deliver extremely high luminosities across multiple energies

## Slide 27
Detailed feasibility study: layout selected from ~100 variants following the EU “Avoid–Reduce–Compensate” principle — 90.7 km ring, 8 surface sites (7 FR, 1 CH), 5.5 m tunnel diameter, 50–560 m depth
FCC-ee
Next-generation circular e+e– collider to deliver extremely high luminosities across multiple energies

## Slide 28
Ring structure: 4 experiments, 1 RF-section / beam, 1 collimation section, 1 section for injection and dump
Booster is single-beam synchrotron which cycles within a few seconds between accelerating and top-up injecting e+ and e–
FCC-ee
Next-generation circular e+e– collider to deliver extremely high luminosities across multiple energies

## Slide 29
Geology of FCC tunnel
FCC inclined at 0.5% gradient to minimise depth of point F
Limestone unavoidable between G–H
Tunneling mainly in molasse layer (soft rock), well suited for fast, low-risk construction, 6 million m3 excavated volume
→ 8.5 million m3 excavation material on surface (OpenSkyLab R&D project to study reuse), average shaft depths ~240 m
265’000 m3 concrete/year over 8 years (0.075% of annual EU production), use of low-carbon concrete under study
FCC-ee
Next-generation circular e+e– collider to deliver extremely high luminosities across multiple energies
Total civil engineering construction carbon footprint estimate: 530,000 – 1,184,000 tCO2(eq)
Assessed according to European Norms (EN 17472, EN15804+A2)
= 1.5 – 3.4 × CERN with LHC operation per year

## Slide 30
FCC-ee — territorial dialogue & public participation
Public information and discussion meetings
First cycle of public information meetings between April 2024 – March 2025
11 sessions reached over 1,500 people in France & Switzerland
During 2025: Second cycle of public information meetings
Workshops with residents in municipalities potentially affected by surface sites; meetings with stakeholders of the territory
May/June – October 2026: Formal public participation process in France (Débat Public) and Switzerland (public concertation)
Workshops with residents in municipalities potentially affected by surface sites; meetings with stakeholders of the territory
Dialogue website:

## Slide 31
FCC-ee collider concept for maximum luminosity
Numbers assume 4 experiments
~350,000 × LEP-1
~5,000 × LEP-2
Double ring collider: many bunches, high current, like LHC and B factories, different from LEP (CERN)
Top-up injection (requiring booster) during collisions: needed due to short luminosity lifetime (~10–20 min, radiative Bhabhas), standard at light sources and used at PEP-II, KEKB, BEPCII. Booster intensity ~1% of collider; full RF voltage as in collider
Superconducting RF: LEP-proven Nb/Cu 400 MHz cavities; bulk Nb 800 MHz cavities as in ESS/EuXFEL; efficient RF sources and simplified energy-switching scheme
Crab-waist collisions: successfully demonstrated at DAΦNE and SuperKEKB
FCC-ee — maximum luminosity
Crab waist scheme: sextupoles near IP rotate vertical waist along the opposing beam’s path (and suppresses beam-beam resonances)

## Slide 32
FCC-ee collider concept for maximum luminosity
Double ring collider: many bunches, high current, like LHC and B factories, different from LEP (CERN)
Top-up injection (requiring booster) during collisions: needed due to short luminosity lifetime (~10–20 min, radiative Bhabhas), standard at light sources and used at PEP-II, KEKB, BEPCII. Booster intensity ~1% of collider; full RF voltage as in collider
Superconducting RF: LEP-proven Nb/Cu 400 MHz cavities; bulk Nb 800 MHz cavities as in ESS/EuXFEL; efficient RF sources and simplified energy-switching scheme
Crab-waist collisions: successfully demonstrated at DAΦNE and SuperKEKB
FCC-ee — maximum luminosity
Crab waist scheme: sextupoles near IP rotate vertical waist along the opposing beam’s path (and suppresses beam-beam resonances)
Combining all these concepts results in a giant efficiency step: 104 – 105 × luminosity / electrical power of LEP

## Slide 33
FCC-ee — SRF
Superconducting RF system — key technology
Ref: arXiv:2505.00274
400 MHz superconducting cavity (6~10 MV/m), copper Nb coated, 1.5 m long
400 MHz Cryo-module
2-cell* 400 MHz SRF system for Z, W and ZH
Higher gradient 6-cell 800 MHz SRF system for tt collider operation and booster at all energies
Compact 800 MHz cavity (~20 MV/m), 6-cell, bulk Nb, Nb3Sn if R&D is successful
800 MHz Cryo-module
× 264
× 66
× (408 + 448 booster)
× (102 + 112 booster)
Power source: 380 kW Klystron prototype built (HL-LHC) η* = 70% → two-stage Klystrons η = 86% → multibeam Tristrons η > 90% (R&D)
× 264
× 204 Tristons +
448 × 10 kW SSA booster
Klystron prototype
*
*A cell is one resonant section of the cavity where acceleration occurs (half a wavelength long = 38 cm for 400 MHz)

## Slide 34
FCC-ee — parameters
FCC-ee main parameters (assuming 4 IPs / experiments)
Parameter | Z | WW | H (ZH) |  | 
Collision energy √s [GeV] | 88, 91, 94 | 157, 163 | 240 | 340–350 | 365
SR energy loss / turn [GeV] | 0.036 | 0.08 | 1.7 | 7.8 | 9.2
Total RF voltage 400 / 800 MHz [GV] | 0.08 / 0 | 1.0 / 0 | 2.1 / 0 | 2.1 / 7.4 | 2.1 / 9.2
Synchrotron radiation/beam [MW] | 50 | 50 | 50 | 50 | 50
Beam current [mA] | 1294 | 135 | 26.8 | 6.0 | 5.1
Number bunches / beam | 11200 | 1852 | 300 | 70 | 64
Luminosity / IP [1034 cm–2s–1] | 144 | 20 | 7.5 | 1.8 | 1.4
Luminosity / year [ab–1] | 68 | 9.6 | 3.6 | 0.83 | 0.67
Run time (including lumi ramp-up) [years] | 4 | 2 | 3 | 1 | 4
Total integrated luminosity [ab–1] | 205 | 19.2 | 10.8 | 0.4 | 2.7
Total number of events | 61012 Z | 2.4108 WW (incl. WW at higher √s) | 2.2106 ZH 65k WW → H | 2106 + 370k ZH + 92k WW → H | 
Parameter | Z | WW | H (ZH) |  | 
Collision energy √s [GeV] | 88, 91, 94 | 157, 163 | 240 | 340–350 | 365
SR energy loss / turn [GeV] | 0.036 | 0.08 | 1.7 | 7.8 | 9.2
Total RF voltage 400 / 800 MHz [GV] | 0.08 / 0 | 1.0 / 0 | 2.1 / 0 | 2.1 / 7.4 | 2.1 / 9.2
Synchrotron radiation/beam [MW] | 50 | 50 | 50 | 50 | 50
Beam current [mA] | 1294 | 135 | 26.8 | 6.0 | 5.1
Number bunches / beam | 11200 | 1852 | 300 | 70 | 64
Luminosity / IP [1034 cm–2s–1] | 144 | 20 | 7.5 | 1.8 | 1.4
Luminosity / year [ab–1] | 68 | 9.6 | 3.6 | 0.83 | 0.67
Run time (including lumi ramp-up) [years] | 4 | 2 | 3 | 1 | 4
Total integrated luminosity [ab–1] | 205 | 19.2 | 10.8 | 0.4 | 2.7
Total number of events |  |  |  |  | 
Ref: arXiv:2505.00274
~350,000 × LEP-1 (~6 years)
~26 × HL-LHC (~9 years)
~5,000 × LEP-2 (~5 years)
0.5% of HL-LHC (~9 years)
0.01% of HL-LHC (tt) (~9 years)
,

## Slide 35
FCC-ee — parameters
FCC-ee main parameters (assuming 4 IPs / experiments)
Parameter | Z | WW | H (ZH) |  | 
Collision energy √s [GeV] | 88, 91, 94 | 157, 163 | 240 | 340–350 | 365
SR energy loss / turn [GeV] | 0.036 | 0.08 | 1.7 | 7.8 | 9.2
Total RF voltage 400 / 800 MHz [GV] | 0.08 / 0 | 1.0 / 0 | 2.1 / 0 | 2.1 / 7.4 | 2.1 / 9.2
Synchrotron radiation/beam [MW] | 50 | 50 | 50 | 50 | 50
Beam current [mA] | 1294 | 135 | 26.8 | 6.0 | 5.1
Number bunches / beam | 11200 | 1852 | 300 | 70 | 64
Luminosity / IP [1034 cm–2s–1] | 144 | 20 | 7.5 | 1.8 | 1.4
Luminosity / year [ab–1] | 68 | 9.6 | 3.6 | 0.83 | 0.67
Run time (including lumi ramp-up) [years] | 4 | 2 | 3 | 1 | 4
Total integrated luminosity [ab–1] | 205 | 19.2 | 10.8 | 0.4 | 2.7
Total number of events | 61012 Z | 2.4108 WW (incl. WW at higher √s) | 2.2106 ZH 65k WW → H | 2106 + 370k ZH + 92k WW → H | 
Parameter | Z | WW | H (ZH) |  | 
Collision energy √s [GeV] | 88, 91, 94 | 157, 163 | 240 | 340–350 | 365
SR energy loss / turn [GeV] | 0.036 | 0.08 | 1.7 | 7.8 | 9.2
Total RF voltage 400 / 800 MHz [GV] | 0.08 / 0 | 1.0 / 0 | 2.1 / 0 | 2.1 / 7.4 | 2.1 / 9.2
Synchrotron radiation/beam [MW] | 50 | 50 | 50 | 50 | 50
Beam current [mA] | 1294 | 135 | 26.8 | 6.0 | 5.1
Number bunches / beam | 11200 | 1852 | 300 | 70 | 64
Luminosity / IP [1034 cm–2s–1] | 144 | 20 | 7.5 | 1.8 | 1.4
Luminosity / year [ab–1] | 68 | 9.6 | 3.6 | 0.83 | 0.67
Run time (including lumi ramp-up) [years] | 4 | 2 | 3 | 1 | 4
Total integrated luminosity [ab–1] | 205 | 19.2 | 10.8 | 0.4 | 2.7
Total number of events |  |  |  |  | 
Ref: arXiv:2505.00274
Despite the constant synchrotron power, due to the larger RF voltage and system size (increased cryogenic system), RF efficiency losses, and other increasing accelerator demands, the electrical power consumption increases with CM energy:
FCC-ee elecrtical energy consumption | Z | W | H | top
Beam energy [GeV] | 45.6 | 80 | 120 | 182.5
Peak power during beam operation [MW] | 250 | 275 | 297 | 381
Total FCC-ee yearly consumption [TWh] | 1.2 | 1.3 | 1.4 | 1.85
LHC + injectors: ~ 200 MW peak power
Today CERN with LHC operating: ~1.3 TWh
Various R&D towards further reduction of electrical energy consumption
,

## Slide 36
FCC-ee — detectors
Event rates and radiation are modest compared with HL-LHC, but Tera-Z precision imposes unprecedented stability and resolution demands: luminosity at 10–5 relative and 10–4 absolute precision, acceptance definition at 10–5, etc. Ultimately, most measurements will be systematics- and theory-limited
Detector concepts are built around high-granularity particle-flow calorimetry, close-to-beam MAPS vertex detectors, large low-material central trackers, PID, a ~2 T solenoid, and muon tagging, with fields up to 3 T possible above the Z pole.
IDEA detector concept around dual-readout (scintillation (all) & Cherenkov (relativistic – e/𝛾) light) fiber/Cu calorimeters [Ref]
ALLEGRO detector concept around noble-liquid EM calorimeter [Ref]
CLD detector concept silicon-tungsten EM calorimeter and tracker [Ref]
*A too-strong detector solenoid (≥ 4 T) would distort the beam trajectories, induce transverse coupling, and blow up the vertical emittance — drastically reducing luminosity
Dual-readout (DR) technique can in principle distinguish between EM and HAD responses in single CAL. Nevertheless, newest IDEA design proposes DR crystal ECAL and DR fibre HCAL

## Slide 37
FCC-ee — Higgs Factory
Primary goal: Higgs precision measurements
e+e– → X cross sections versus CM energy
W-boson fusion (6.7 fb)
(Z-boson fusion 0.63 fb)
WBF: — e+/e– radiate W/Z, which increases with energy
HZ factory
Simulated e+e– → ZH event at √s = 240 GeV in IDEA detector
Higgsstrahlung (σ = 232 fb at √s = 240 GeV)
s-channel: — falling off a resonance

## Slide 38
FCC-ee — Higgs Factory
Absolute coupling strengths — difficult at LHC due to weak constraint on (current precision ~50%, HL-LHC < 25%)
Higgsstrahlung (σ = 232 fb at √s = 240 GeV)
arXiv:2106.15438
Combination with measurement of
allows to determine to 0.8% precision (30 × HL-LHC)
Can measure total HZ cross section and hence (0.1% precision) independently of Higgs decays via recoil mass (Mrecoil) by counting events with an identified Z → 𝓁𝓁
Standard reference to be used by all other Higgs coupling measurements

## Slide 39
FCC-ee – the Higgs factory
Why “factory”? 2.2M Higgs (FCC-ee) vs 350M (HL-LHC), production through Higgsstrahlung rather than s-channel
→ e+e– collisions offer exceptionally clean Higgs reconstruction, unmatched precision on decays with large branching ratios
HL-LHC numbers updated from arXiv:2504.00672; they assume SM value for , and incl. theoretical uncertainties (mostly dominant)
Note: current uncertainties on Higgs branching fraction predictions O(1.5%)
1.6
1.6
3.6
2.4
1.9
~ 40
1.8
6.8
3.4
3.0
–
< 25
0.025
0.04
FCC-ee feasibility stydu (Vol 1): arXiv:2505.00272
16
5.5
7.3
4.4
4.1
~ 44
1.6
1.6
1.1
0.9
–
< 32
50
5.9
*
*Incl. SM parametric uncertainties
Uncertainty
HL-LHC / FCC-ee
Most precise coupling, probes
Particularly large improvement over HL-LHC
BR(H → 4𝜈) = 10.6 10–4

## Slide 40
FCC-ee – the Higgs factory
Why “factory”? 2.2M Higgs (FCC-ee) vs 350M (HL-LHC), production through Higgsstrahlung rather than s-channel
→ e+e– collisions offer exceptionally clean Higgs reconstruction, unmatched precision on decays with large BR
1.6
1.6
3.6
2.4
1.9
~ 40
1.8
6.8
3.4
3.0
–
< 25
0.025
0.04
FCC-ee feasibility stydu (Vol 1): arXiv:2505.00272
16
5.5
7.3
4.4
4.1
~ 44
1.6
1.6
1.1
0.9
–
< 32
50
5.9
*
Uncertainty
HL-LHC / FCC-ee
BR(H → 4𝜈) = 10.6 10–4
Collider limits overlaid onto direct detection (Higgs portal assuming Majorana DM)

## Slide 41
FCC-ee – also a Tera-Z, W and top factory
Input to global electroweak fit: requires significant improvements in theoretical predictions
Improvements up to × 500 over current knowledge
arXiv:2505.00272
Extreme luminosity on Z pole: 1401034 cm–2s–1 / IP, 205 ab–1 & 61012 Z (4 IPs) — ultimate EW precision data

## Slide 42
FCC-ee – also a Tera-Z, W and top factory
Global electroweak fit expressed on top versus W mass
Conservative theoretical uncertainty scenario
ESPPU 2025 Briefing Book and R. Kogler at Moriond EW 2026

## Slide 43
FCC-ee – also a Tera-Z, W and top factory
Global electroweak fit: indirect constraints on new physics via “oblique parameters”
ESPPU 2025 Briefing Book and R. Kogler at Moriond EW 2026
Conservative theoretical uncertainty scenario

## Slide 44
FCC-ee – also a flavour factory (on Z pole)
–
–
BR(Z → bb / cc) = 15% / 12%
Γ(Z → qq) ∝
Yields for 61012 Z
Belle-II (×109) 28 28 – – – 33 46
Yields for 50 ab–1
Clean reconstruction due to boost and flavour tagging (> LHCb), excellent charm / 𝜏 separation (challenging at ϒ(4S))
Ultimate CKM angle precision (similar to LHCb)
Ultimate τ factory
The larger yield of B mesons than Belle II allows unmatched precision on B decays with neutrinos
FCC-ee (×109)
B → 𝜏𝜈 allows 1% measurement of |Vub| and running above WW threshold allows on-shell measurement of |Vcb| to ~1%
Current precision 3.5Vub / 1.1Vcb%, but discrepancies between exclusive and inclusive results of 17Vub / 5Vcb%, respectively
arXiv:2505.00272
Large c and b-hadron statistics — combines strengths of Belle-II (e+e– → ϒ(4S) → BB) and LHCb (pp → bb + X)

## Slide 45
FCC-ee — projected construction cost
First stage incl. Z, WW and ZH working points. Upgrade to ttbar adds 1,260 MCHF
Domain | Cost [MCHF]
Civil engineering | 6,160
Technical infrastructures | 2,840
Injectors and transfer lines | 590
Booster and collider | 4,140
CERN contribution to four experiments | 290
FCC-ee total | 14,020
+ four experiments (non-CERN part) | 1,300
FCC-ee total incl. four experiments | 15,320
Human resources for construction estimated to 15,000 FTE-years
Over a period of 15 years
Note: First FCC-ee stage (up to ZH)

## Slide 46
FCC-ee — projected construction cost
First stage incl. Z, WW and ZH working points. Upgrade to ttbar adds 1,260 MCHF
Socio-economic impact analysis (incl. investment, personnel, external effects, dismantling, …) estimates benefit–cost factor of 1.2 (net: 4.1 MCHF)
https://doi.org/10.5281/zenodo.10653395
90% CL lower limit
Domain | Cost [MCHF]
Civil engineering | 6,160
Technical infrastructures | 2,840
Injectors and transfer lines | 590
Booster and collider | 4,140
CERN contribution to four experiments | 290
FCC-ee total | 14,020
+ four experiments (non-CERN part) | 1,300
FCC-ee total incl. four experiments | 15,320
Human resources for construction estimated to 15,000 FTE-years
Over a period of 15 years
Note: First FCC-ee stage (up to ZH)

## Slide 47
FCC — timeline of integrated programme
FCC-ee followed by FCC-hh
2033–2041 civil engineering construction work
2039–2043 technical infrastructure installation
2041–2045 accelerator installation
Reference design phase
European strategy recommendation

## Slide 48
FCC-ee — global collaboration
Increasing international collaboration is a prerequisite for success. Links with science, R&D, and high-tech industry will be essential to further advance and prepare the implementation of the FCC
38 Countries (162 Institutes)
Austria – Belgium – Brazil – Canada – CERN – Chile – Colombia – Czech Republic – Denmark – Estonia – Finland – France – Georgia – Germany – Greece – Hungary – India – Iran – Italy – Japan – Latvia – Malta – Mexico – Netherlands – Norway – Pakistan – Poland – Portugal – Republic of Korea – Romania – Serbia – Spain – Sweden – Switzerland – Thailand – Türkiye – Ukraine – United Kingdom – United States of America

## Slide 49
European Commission — moonshots
Recognition by the European Commission highlights the strategic value of the FCC, not only for fundamental research but also as a project fostering high-level collaboration in Europe
Link to document

## Slide 50
FCC-ee is Europe’s priority for CERN’s next collider project: a transformative instrument for exploring the Higgs boson, the electroweak sector, and the quantum structure of fundamental interactions with unprecedented precision
A detailed feasibility study has been released, and the project is now moving toward the next design phase, with a possible CERN Council decision around 2028
FCC-ee is also the foundation for the future energy frontier, enabling a subsequent hadron collider in the same infrastructure — a highly synergistic and complementary programme that maximises the long-term physics reach
Sustainability is a design principle, not an afterthought, embedded in the FCC-ee study from the outset
Conclusions

## Slide 51
Extra slides …

## Slide 52
FCC-ee — projected acceptance
Does the average taxpayer in CERN’s member states support a new accelerator at CERN?
A public perception study assessed quantitative indicators for drivers as basis for evidence-based actions
How much of their taxes would citizens be willing to allocate to a new collider project at CERN?
Study based on accredited methodology, passed through an ethics committee and carried out with an independent, domain specific quality management certified support company.
Link to article: https://inspirehep.net/literature/3155013
In general, the offered amounts exceed significantly the actual contribution of a taxpayer to CERN
66% of respondents expressed their willingness to financially support a new collider at CERN with their annual taxes. 34% reported zero willingness to support
Positive opinions raised from 58% to 78%, negative fell from 18% to 2% after receiving specific CERN related information

## Slide 53
HL-LHC Physics prospects — Higgs
Higgs coupling prospects | Coupling strength modifiers (, assuming SM )
Unique sensitivity to rare decays and to top coupling
In SILH 5.0% (1.6%) precision on probes compositeness scale 1.1 (1.9) TeV
Prospects for Higgs width from off-shell measurement, invisible Higgs decays, Higgs sector extensions (2HDM)
ΓH via μoff-shell / μon-shell in H → 4𝓁 & 2𝓁2𝜈 with < 20% uncertainty
BR(H → invisible) < 2.5%
Discover or exclude MSSM two Higgs doublets scenario deep into TeV scale for tanβ > 6
Even with 2× better theory precision, theoretical uncertainties will be dominant
53

## Slide 54
HL-LHC Physics prospects — Higgs
Higgs self-coupling via Higgs pair production: complex final states, eldorado for ML enthusiasts, strongest channels: HH → bb𝛾𝛾, bb𝜏𝜏, bbbb. Best sensitivity to at low m(HH)
For SM:
Expect HH observation > 7σ
precision better than 30%
t
arXiv:2504.00672

## Slide 55
FCC-ee – Injector
FCC-ee injector with high-energy linac
Located on CERN Prévessin site
Transfer line to FCC PA (LHC P8, LHCb), “cut and cover” construction
Conventional positron source using tungsten target + capture linac, need: 1.1⨯1013 e+/s (SLC: ∼6 ⨯1012 e+/s)
2.9 GeV damping ring with wigglers (small synchrotron to reduce transverse and longitudinal beam emittance)
Main linac ~1 km with 22.5 MV/m to accelerate e+ and e– to 20 GeV for injection into booster
Total length about 1.2 km
SPS
FCC
Damping ring

## Slide 56
FCC-ee — parameters
FCC-ee main parameters (assuming 4 IPs / experiments)
Parameter | Z | WW | H (ZH) |  | 
Collision energy √s [GeV] | 88, 91, 94 | 157, 163 | 240 | 340–350 | 365
SR energy loss / turn [GeV] | 0.036 | 0.08 | 1.7 | 7.8 | 9.2
Total RF voltage 400 / 800 MHz [GV] | 0.08 / 0 | 1.0 / 0 | 2.1 / 0 | 2.1 / 7.4 | 2.1 / 9.2
Synchrotron radiation/beam [MW] | 50 | 50 | 50 | 50 | 50
Beam current [mA] | 1294 | 135 | 26.8 | 6.0 | 5.1
Number bunches / beam | 11200 | 1852 | 300 | 70 | 64
Luminosity / IP [1034 cm–2s–1] | 144 | 20 | 7.5 | 1.8 | 1.4
Luminosity / year [ab–1] | 68 | 9.6 | 3.6 | 0.83 | 0.67
Run time (including lumi ramp-up) [years] | 4 | 2 | 3 | 1 | 4
Total integrated luminosity [ab–1] | 205 | 19.2 | 10.8 | 0.4 | 2.7
Total number of events | 61012 Z | 2.4108 WW (incl. WW at higher √s) | 2.2106 ZH 65k WW → H | 2106 + 370k ZH + 92k WW → H | 
Parameter | Z | WW | H (ZH) |  | 
Collision energy √s [GeV] | 88, 91, 94 | 157, 163 | 240 | 340–350 | 365
SR energy loss / turn [GeV] | 0.036 | 0.08 | 1.7 | 7.8 | 9.2
Total RF voltage 400 / 800 MHz [GV] | 0.08 / 0 | 1.0 / 0 | 2.1 / 0 | 2.1 / 7.4 | 2.1 / 9.2
Synchrotron radiation/beam [MW] | 50 | 50 | 50 | 50 | 50
Beam current [mA] | 1294 | 135 | 26.8 | 6.0 | 5.1
Number bunches / beam | 11200 | 1852 | 300 | 70 | 64
Luminosity / IP [1034 cm–2s–1] | 144 | 20 | 7.5 | 1.8 | 1.4
Luminosity / year [ab–1] | 68 | 9.6 | 3.6 | 0.83 | 0.67
Run time (including lumi ramp-up) [years] | 4 | 2 | 3 | 1 | 4
Total integrated luminosity [ab–1] | 205 | 19.2 | 10.8 | 0.4 | 2.7
Total number of events |  |  |  |  | 
Ref: arXiv:2505.00274
Despite the constant synchrotron power (, ), due to the larger RF voltage and system size (increased cryogenic system), RF efficiency losses, and other increasing accelerator demands, the electrical power consumption increases with CM energy:
FCC-ee electrical energy consumption | Z | W | H | top
Beam energy [GeV] | 45.6 | 80 | 120 | 182.5
Peak power during beam operation [MW] | 250 | 275 | 297 | 381
Total FCC-ee yearly consumption [TWh] | 1.2 | 1.3 | 1.4 | 1.85
LHC + injectors: ~ 200 MW peak power
Today with LHC operating: ~1.3 TWh
Various R&D towards further reduction of electrical energy consumption
Global data-centre electricity use is projected to rise from 460 TWh in 2024 (1.5% of total electricity consumption) to 1,000 TWh (±25%) by 2030 and 1,300 (±40%) TWh by 2035 (~15% annual raise), driven mainly by the US and China. The AI share may grow from 10~20% today to 30~50% in 2035.
Reference: International Energy Agency,
see also this critical review of the modelling
Aerial view of Microsoft’s new AI datacenter in Mt Pleasant, Wisconsin, Sep 2025 [Link]

## Slide 57
FCC-ee — beam energy
Precise knowledge of beam energy at Z pole crucial, meticulous work done at LEP to achieve
mZ ΓZ
LEP ECM related syst. uncertainty: 1.7 MeV (1.9 × 10–5) 1.2 MeV
FCC-ee statistical uncertainty: 4 keV (≪ 10–6) 4 keV
Precise beam energy calibration (ΔE/E < 10–6) through resonant depolarisation (RDP) as previously done at VEPP-2M (Novosibirsk) and LEP
Due to synchrotron radiation, e± in storage ring become transversely polarised with a spin tune (number of spin precessions per turn in the bending field): . By applying an external RF field tuned to , which depolarises the beam, can be measured with extraordinary precision
At LEP, RDP could only be performed in a few fills, before or after collisions. ECM knowledge limited by modelling of time evolution between measurements. ECM calibration must be a central consideration in FCC-ee design & operational strategy: quasi-continuous RDP using non-colliding (unpaired) bunches
Expect that ECM systematics can be limited to 100 keV on mZ and 25 keV on ΓZ
Beam energy variation at LEP from Earth tides
~ 9 MeV
See, eg, this CERN Courier article

## Slide 58
FCC-ee – also a Tera-Z, W and top factory
arXiv:2505.00272
Extreme luminosity on Z pole: 1401034 cm–2s–1 / IP, 205 ab–1 & 61012 Z (4 IPs) — ultimate EW precision data
Simulation of tt threshold scan with CLIC [arXiv:2503.24168]
Improvements up to × 2000 over current knowledge

## Slide 59
FCC-ee – the Higgs factory
✅
✅
✅
✅
❓
✅
✅
✅
✅
✅
✅
✅
Almost all Higgs couplings to SM particles will have been measured at HL-LHC & FCC-ee
Can we measure the decay? (recall: = 4.1 MeV)
The entire HL-LHC may produce 2 such events!
At the FCC-ee, BW s-channel resonance:
but ISR and √s spread will lead to smearing of BW peak, so that effective cross section is 0.3 fb (remember: LZH = 10.8 ab–1). Can it be done?
Extremely challenging — cornering the electron Yukawa coupling:

## Slide 60
FCC-ee – the Higgs factory
Can we measure the decay? (recall: = 4.1 MeV)
The entire HL-LHC may produce 2 such events!
At the FCC-ee, BW s-channel resonance:
but ISR and √s spread will lead to smearing of BW peak, so that effective cross section is 0.3 fb (remember: LZH = 10.8 ab–1). Can it be done?
Requires precise knowledge of Higgs mass to few MeV
Beam must be monochromatized to match narrow [arXiv: 2411.04210]
arXiv:2107.02686
Possible sensitivity to of ~0.5σ per year and IP
Correlate energy and transverse position so high-energy particles collide with low-energy ones (opposite beam dispersions at IP) — requires dedicated instruments: proposed for many e+e– colliders, but never implemented
Extremely challenging — cornering the electron Yukawa coupling:

## Slide 61
FCC-ee – the Higgs factory
Higgs self-coupling — no HH production at FCC-ee, sensitivity through H–H–H loops
FCC-ee+hh tightly constrains BSM models with 1st order EW phase transition
NLO vertex corrections to Higgsstrahlung (similar for W-boson fusion)
arXiv:1711.03978
Measuring σ(e+e– → ZH) and σ(e+e– → 𝜈𝜈H) at different √s improves precision on from 30% (HL-LHC) to 20% (or 40% standalone) in EFT analysis
arXiv:2504.00672

## Slide 62
Power efficiency: next-generation e+e– collider
Figure reference
FCC-ee vs LEP: larger bending radius, more efficient superconducting RF, improved beam optics (higher beam-beam performance limits), ultra-low emittance magnet lattices, crab waist scheme, continuous top-up injection via booster (always near optimal luminosity), power-optimised from the start
FCC-ee delivers 104 – 105 × luminosity / electrical power of LEP

## Slide 63
Project | Construction start | First beams | Peak lumi at Z per IP [1034 cm–2s–1] | Peak lumi at HZ per IP [1034 cm–2s–1] | Years of operation | Construction cost* [BCHF] | Next stage collider | Start of operation | Total construction cost* [BCHF]
FCC-ee | 2033 | 2046 | 144 | 7.5 | 14 | 15.3 | FCC-hh | 2079 | 34.7
LEP3 | 2037 | 2047 | 40 | 1.6 | 15 | 4.1 | FCC-hh | 2074 | 32.5
LCF 250 → 550 GeV | 2035 | 2045 | 0.28 | 1.4 – 2.7 | 19 | 9.4 + 5.4 = 14.8 | > 1 TeV collider? | – | –
CLIC 380 → 1500 GeV | 2035 | 2045 | – | 1.2380 GeV | 20 | 7.5 + 7.1 = 14.6 | 3 TeV collider? | – | –
LHeC | 2037 | 2044 | – | 2.3 | 7 | 2.1 | FCC-hh | 2064 | 30.5
*Construction costs include experiments
Similar start dates driven by HL-LHC running until 2041
The big picture: next-generation collider projects for CERN

## Slide 64
Intermediate conclusions by ESG
[Link to document]
FCC-ee is technically feasible and would deliver the broadest high-precision particle physics programme. It would also pave the way towards a hadron collider reusing the tunnel and much of the infrastructure
LEP3 and LHeC as alternative options with significantly lower construction cost (but no new tunnel for a possible hadron collider): not competitive with FCC-ee on breadth of physics programme, not flagship colliders
CLIC and LCF as alternative options: operation at 550 GeV or higher would offer competitive programmes in Higgs and top-quark physics, however, overall not competitive with FCC-ee. Both require a new tunnel of about 33 km to reach their ultimate energies. Path to 10 TeV pCM requires plasma wakefield acceleration, which is not yet a proven technology
Descoped FCC-ee to reduce cost by 15% (no ttbar run: –1.26 BCHF, drop 2 / 4 experiments: –0.80 BCHF, decrease RF power from 50 → 30 MW (–0.35 BCHF) significantly impacts breadth of the physics programme and precision, but still stronger than other options. Scenarios would be reversible
[ L(FCC-ee) × 3/5 × 2/4 × 1.2 = L(FCC-ee) × 0.36 → need to run 2.8 × longer for equivalent physics ]

## Slide 65
ESG recommendations
[Link to document, Karl’s talk]
General Recommendations

## Slide 66
ESG recommendations
[Link to document, Karl’s talk]
The next CERN flagship collider project

## Slide 67
ESG recommendations
[Link to document, Karl’s talk]
Technology

## Slide 68
The European Strategy for Particle Physics – Update (ESPPU)
From Karl’s talk

## Slide 69
Overall summary
[From Karl’s talk]
Physics: from WG2b: sum of precision/BSM physics
Phys vs CEPC: competitiveness, assuming CEPC is running in parallel
Tech readiness: from WG2a
Construction cost: from proponents + exp. (CERN part)

## Slide 70
LEP3 — a Higgs and EW factory in the LHC tunnel
Backup if (preferred) FCC-ee cannot be realised with long-term goal of an energy-frontier hadron or muon collider: similar to FCC-ee with booster and collider rings, 2 beampipes, 50 MW / beam, 2 IPs
Challenges for LEP3 include design of IRs, large E-loss, need 6.0 GV RF power installed in 4 long straight sections (2 booster, 2 collider), crab-waist scheme requires large crossing angle and widening tunnel on either side of the experiments from ~4m to 7m diameter along 270 m
Parameter | Z | WW | H (ZH) |  | 
Inst. luminosity / IP [1034 cm–2s–1] | 40 | 6.2 (160 GeV) | 1.6 (230 GeV) | – | 
SR energy loss / turn [GeV] | 0.13 | 1.3 | 5.4 | (~25 GeV) | 
Integrated luminosity / year / IP [ab–1] | 4.8 | 0.7 | 0.19 | – | 
Run time [years] | 5 | 4 | 6 | – | 
Total integrated luminosity [ab–1, 2 IPs] | 48 | 6.0 | 2.3 | – | 
Total number of events [2 IPs] | 1.41012 | 0.36108 | 0.42106 | – | 
Inst. luminosity / IP [1034 cm–2s–1] | 144 | 20 (157, 163 GeV) | 7.5 (240 GeV) | 1.8 (~350 GeV) | 1.4 (365 GeV)
SR energy loss / turn [GeV] | 0.036 | 0.08 | 1.7 | 7.8 | 9.2
Integrated luminosity / year / IP [ab–1] | 17 | 2.4 | 0.9 | 0.21 | 0.17
Run time (including lumi ramp-up) [years] | 4 | 2 | 3 | 1 | 4
Total integrated luminosity [ab–1, 4 IPs] | 205 | 19.2 | 10.8 | 0.4 | 2.7
Total number of events [4 IPs] | 61012 | 2.4108 | 2.2106 | 2106 | 
Parameter | Z | WW | H (ZH) |  | 
Inst. luminosity / IP [1034 cm–2s–1] | 40 | 6.2 (160 GeV) | 1.6 (230 GeV) | – | 
SR energy loss / turn [GeV] | 0.13 | 1.3 | 5.4 | (~25 GeV) | 
Integrated luminosity / year / IP [ab–1] | 4.8 | 0.7 | 0.19 | – | 
Run time [years] | 5 | 4 | 6 | – | 
Total integrated luminosity [ab–1, 2 IPs] | 48 | 6.0 | 2.3 | – | 
Total number of events [2 IPs] |  |  |  | – | 
Inst. luminosity / IP [1034 cm–2s–1] | 144 | 20 (157, 163 GeV) | 7.5 (240 GeV) | 1.8 (~350 GeV) | 1.4 (365 GeV)
SR energy loss / turn [GeV] | 0.036 | 0.08 | 1.7 | 7.8 | 9.2
Integrated luminosity / year / IP [ab–1] | 17 | 2.4 | 0.9 | 0.21 | 0.17
Run time (including lumi ramp-up) [years] | 4 | 2 | 3 | 1 | 4
Total integrated luminosity [ab–1, 4 IPs] | 205 | 19.2 | 10.8 | 0.4 | 2.7
Total number of events [4 IPs] |  |  |  |  | 
LEP3
FCC-ee
Total cost 3.7B CHF
ESPPU input: arXiv:2504.00541
Construction:
FCC-ee SR loss reference
Total cost 13.7B + 1.3Btt CHF

## Slide 71
Linear Collider Facility (LCF) at CERN
Very similar to ILC: baseline is 33.5 km tunnel, SRF cavities with an accelerating gradient of 31.5 MV m−1, √s = 250 GeV upgradable to 550 GeV, longitudinal polarisation (± 80/30% for e–/e+, ~20% higher σ(ZH)), 2 IPs (sharing luminosity)
ESPPU input: arXiv:2503.19983
Parameter | Z | WW | H (ZH) | above | 
Inst. luminosity / IP [1034 cm–2s–1] | 0.28 | – | 1.4LP / 2.7FP (250 GeV) | 3.9 (550 GeV) | 
Integrated luminosity / year / IP [ab–1] | 30 | – | 0.19LP + 0.64FP | 2.3 | 
Run time [years] | 1 | – | 5LP + 3FP | 10 | 
Total integrated luminosity [ab–1, 2 IPs*] | 0.07 | – | 1.0LP + 1.9FP | 8.3 | 
Total number of events [2 IPs*] | 0.0021012 | – | 0.8106 | ~ 1.6 (H) / 3.9 (tt)106 | 
Inst. luminosity / IP [1034 cm–2s–1] | 144 | 20 (157, 163 GeV) | 7.5 (240 GeV) | 1.8 (~350 GeV) | 1.4 (365 GeV)
Integrated luminosity / year / IP [ab–1] | 17 | 2.4 | 0.9 | 0.21 | 0.17
Run time (including lumi ramp-up) [years] | 4 | 2 | 3 | 1 | 4
Total integrated luminosity [ab–1, 4 IPs] | 205 | 19.2 | 10.8 | 0.4 | 2.7
Total number of events [4 IPs] | 61012 | 2.4108 | 2.2106 | 2106 | 
Parameter | Z | WW | H (ZH) |  | 
Inst. luminosity / IP [1034 cm–2s–1] | 0.28 | – | 1.4LP / 2.7FP (250 GeV) | 3.9 (550 GeV) | 
Integrated luminosity / year / IP [ab–1] | 30 | – | 0.19LP + 0.64FP | 2.3 | 
Run time [years] | 1 | – | 5LP + 3FP | 10 | 
Total integrated luminosity [ab–1, 2 IPs*] | 0.07 | – | 1.0LP + 1.9FP | 8.3 | 
Total number of events [2 IPs*] |  | – |  |  | 
Inst. luminosity / IP [1034 cm–2s–1] | 144 | 20 (157, 163 GeV) | 7.5 (240 GeV) | 1.8 (~350 GeV) | 1.4 (365 GeV)
Integrated luminosity / year / IP [ab–1] | 17 | 2.4 | 0.9 | 0.21 | 0.17
Run time (including lumi ramp-up) [years] | 4 | 2 | 3 | 1 | 4
Total integrated luminosity [ab–1, 4 IPs] | 205 | 19.2 | 10.8 | 0.4 | 2.7
Total number of events [4 IPs] |  |  |  |  | 
LCF
FCC-ee
Total cost:
8.5B CHF (250 GeV, LP)
9.3B CHF (250 GeV, FP)
14.8B CHF (550 GeV)
Total cost 15.3B CHF
Construction:
Challenges for for LCF include the positron source, final focus and nano-beam stability ( ~ 6–8 nm, FCC-ee: 40 nm)
Options to increase energy beyond 550 GeV with development and installation of higher gradient accelerating technologies (see here for a discussion of options)
*LCF proposes to share luminosity among two interaction regions, ie, same integrated luminosity as for single IP